## Slide 1: VAT IC2 Controller Generation
Leo Marugg
22.08.2013

## Slide 2: Background
Actual IC Controller Platform
12 year old design
Some components are reaching end of the lifecycle  difficult component supply
Computing power of 16Bit CPU  Limitation for improving software performance
Fieldbus integration  Expensive solution with OEM-modules
Drive technology  Limited dynamics with present technology
High manufacturing cost  Some expensive components  Logistic costs due to high number of HW-versions

## Slide 3: Target for new Controller Generation
Main topics
Use of latest electronics technology  assures supply security
32Bit CPU technology  Improved computing power for future software developments
Chip based fieldbus integration  Lower cost for fieldbus interfaces
Field orientated drive technology  higher dynamics and more efficient drives
USB service port  Actual Laptop PC can be uses without Adapter
New modular system  reduce logistic cost
VAT wide controller concept  Concept can also cover non control valve applications

## Slide 4: CPU
New 32 Bit CPU
Renesas (JP)
RX600 Family
R63N
Main Features - 100 MHz clock frequency - 1 Mbyt Flash (program code) - 128 kbyte RAM (data memory) - 32 kbyte EEPROM (non volatile memory) - Integrated USB communication unit - up to 13 integrated serial communication units (SPI,RSPI, UART, I2C, CAN, …) - Integrated A/D, D/A converters - Integrated temperature sensor

## Slide 5: Fieldbus Integration
netX52
Hilscher (D)
netX Family
netX52
Supported fieldbuses - EtherCAT - DeviceNet - CC-Link - Profibus - …
Advantages for VAT - Easy to integrate - Low cost

## Slide 6: Motor driver
Nanotec Motion Controller
Standard 32bit micro controller
Nanotec firmware
Field orientated motor control ● High peek torque ● High dynamic (speed, acceleration) ● low power consumption ● torque control ● Load feedback ● smooth movement
Two axes synchronized motion
Advantages for VAT - Easy to integrate - Low cost

## Slide 7: USB Service Interface
USB 2.0 with type B connector
Functionality ● Local control ● Setup ● Diagnostic ● Firmware download (controller, CPA, motion controller, netX)
CPA ● Software stored in controller ● Automatic upload and start after PC-connection ● No installation on PC required ● CPA automatically adapts to controller firmware functionality

## Slide 8: Power Connector
Funktion | Pin |  | Funktion | Regelventil | Isolationsventil
+24V | 1 |  |  | X | X
 |  | 9 | +15V | X | 
+24V | 2 |  |  | X | X
 |  | 10 | -15V | X | 
GND | 3 |  |  | X | X
 |  | 11 | Input Enable (HW) | X | X
GND | 4 |  |  | X | X
 |  | 12 | Input Open | X | X
Output Open | 5 |  |  | X | X
 |  | 13 | Input Close | X | X
Output Closed | 6 |  |  | X | X
 |  | 14 | Input Common (VC) | X | X
Output Common | 7 |  |  | X | X
 |  | 15 | Reserve | Opt. | z.B. Input 3
Reserve | 8 |  |  | Opt. | z.B. Input 4

## Slide 9: Block Diagram

## Slide 10: Basic Concept

## Slide 11: Mechanical Design

## Slide 12: Mechanical Design

## Slide 13: Mechanical Design